## Slide 1
Optical Device Design Based on Automatic Differentiation Programming
汇报人：高博 何家阳

## Slide 2
Background
Related Work
System Design
Evaluation
Conclusion and Future Work
Contents
1

## Slide 3
Advancements in modern optical systems and devices have significantly propelled developments across various fields
  Telecommunications, biosensing, energy-saving
Traditional design paradigm of optical devices faces challenges.
  Demand for smaller, more efficient, and more powerful optical components
  Computational resources and efficiency
Backgroud
2

## Slide 4
Inverse Design
  Deep Learning
  Automatic Differentiation (AD)
    Compute the gradients of the objective function with respect to all the design parameters
Backgroud
3

## Slide 5
Ray-tracing
  Based on geometric optics
  Excellent performance in lens components and illumination systems
  Difficulties in capturing wave phenomena
Related Work
[1] Wu Chang-Mao, Tang Xiong-Xin, Xia Yuan-Yuan, Yang Han-Xiang, and Xu Fan-Jiang. High precision ray tracing method for space camera in optical design. ACTA PHYSICA SINICA, 72(8), 2023.
4

## Slide 6
Full-wave simulation techniques
  Numerically solving Maxwell’s equations
  Accurate simulation of nanophotonic devices
  Unable to provide guidance on how to modify the device
  Manual adjustment, heavily dependent on the experience of the engineer
Related Work
[2] K.S. Yee and J.S. Chen. The finite-difference time-domain (fdtd) and the finite-volume time-domain (fvtd) methods in solving maxwell’s equations. IEEE Transactions on Antennas and Propagation, 45(3):354–363, 1997.
5

## Slide 7
Neural network
  End-to-end machine learning approach
  High accuracy
  Poor interpretability
Related Work
[3] Dianjing Liu, Yixuan Tan, Erfan Khoram, and Zongfu Yu. Training deep neural networks for the inverse design of nanophotonic structures. ACS Photonics, 5(4):1365–1369, Apr 2018.
6

## Slide 8
We target at a novel paradigm for optical device design
  High accuracy
  Automatic design
  Maintain interpretability
  Low computational resource requirements
System Design
7

## Slide 9
Optical device Design based on automatic Differentiation Programming
  Julia
  Spatial discretization
  Forward simulation
  Back propagation
System Design
8

## Slide 10
System Workflow
  Spatial discretization
  Forward simulation
  Back propagation
System Design
9

## Slide 11
Based on inverse design simulation with Julia
Evaluation of optical conponents
  Demultiplexer
  Symmetric crossing
  1x2 splitter
  MMI 1x2 splitter
Design objectives, key parameters, optimization performance, efficiency.
10
Evaluation

## Slide 12
1)Demultiplexer
Frame Design Simulated permittivity
The demultiplexer separates distinct optical signals in wavelength division multiplexing systems based on their different wavelengths.
11

## Slide 13
1)Demultiplexer
Target: 1.1-1.2 μm (Port 2) & 1.8-1.9 μm (Port 3)。
                Optimization Results
O2 port
O3 port
Parameters:
1.Size: 5.0 μm x 2.0 μm
2.Waveguide width: 0.5 μm
3.Internal core of 0.22 μm silicon, outer layer of SiO2 cladding(包层)
4.Minimum Feature: 0.2 μm
Optimizing target setting
T(o2,o1)=1 , T(o3,o1) = 1
Optimizing Results:
T(o2,o1) ~0.99, T(o3,o1) ~0.94
41 iterations, ~123 min
12

## Slide 14
2)Symmetric Crossing
Enables efficient, low-crosstalk, and low-loss Transmission in photonic integrated circuits.
Frame Design Simulated permittivity

## Slide 15
2)Crossing
Optimizing target setting:
T(o3,o1)=1 , T(o2,o1) = T(o4,o1) = 0
Optimizing Results:
Crosstalk is less than 0.01141 .
6 iterations,~68 min
Parameters:
1.Size: 3.5 μm x 3.5 μm
2.Waveguide width: 0.5 μm
3.Internal core of 0.22 μm silicon, outer layer of SiO2 cladding(
4.Minimum Feature: 0.2 μm

## Slide 16
3)1x2 Splitter
The splitter divides an incoming optical signal into two or more output signals.
Frame Design Simulated permittivity
15

## Slide 17
3)1x2 Splitter
Optimization Results
Optimizing target setting:
(Including y-symmetry)
T(o2,o1) = T(o3,o1) =0.5
Optimizing Results:
T(o2, o1) = 0.518
6 iterations,~24 min
16
Parameters:
1.Size: 4.0 μm x 2.0 μm
2.Waveguide width: 0.5 μm
3.Internal core of 0.22 μm silicon, outer layer of SiO2 cladding
4.Minimum Feature: 0.15 μm
5.using a 1.55 μm wavelength beam

## Slide 18
4)MMI 1x2 Splitter
Frame Design Simulated permittivity
A multi-mode interference (MMI) splitter divides an incoming optical signal into multiple output signals by utilizing the interference effects of different modes within a multi-mode waveguide.

## Slide 19
4)MMI 1x2 Splitter
Optimization Results
Optimizing target setting:
(Including y-symmetry)
T(o2,o1) = T(o3,o1) =0.5
Optimizing Results:
T(o2, o1) = 0.311
T(o3, o1) = 0.328(optimization is required)
96 iterations,~143 min
Parameters:
1.Size: 4.0 μm x 2.0 μm
2.Waveguide width: 0.45 μm
3.Internal core of 0.22 μm silicon, outer layer of SiO2 cladding
4.Minimum Feature: 0.15 μm
5.using a 1.55 μm wavelength beam

## Slide 20
Conclusion and Future Work
Julia AD + adjoint optimization = efficient inverse design of integrated optical components.
Julia's native AD significantly accelerates gradient computation, enabling faster design.
Traditional optical design software such as Lumerical FDTD runs slowly on CPUs due to complex gradient calculations.
All designed devices are high-performance, except for MMI.
19

## Slide 21
20
Conclusion and Future Work
GPU Acceleration
Optimize the parameters of design components
Design of more complex components

## Slide 22
Reference

## Slide 23
谢谢！